## Slide 1: H.323
Dr. Quang Duc Tran

## Slide 2: H.323 Definition
H.323 is a ITU-T Recommendation that specifies the components, protocols and procedures that provide multimedia communication services, including real-time audio, video and data communication.
It is widely used within various Internet real-time applications, such as NetMeeting.
H.323 is a part of the ITU-T H.32x series of protocols, which address multimedia communications over ISDN, PSTN and 3G mobile networks.

## Slide 3: H.323 Elements
H.323
Terminal
H.323 Multipoint
Control Unit (MCU)
H.323
Gatekeeper
H.323
Gateway
H.323
Terminal
H.323
Terminal
PSTN
V.70
Terminal
H.324
Terminal
Speech
Terminal
N-ISDN
B-ISDN
QoS
LAN
H.322
Terminal
Speech
Terminal
H.320
Terminal
H.321
Terminal

## Slide 4: H.323 Terminal
H.323 terminal can be either a personal computer (PC) or a stand-alone device, running H.323 and the multimedia application.
H.323 terminal supports audio communication and optionally supports video and data communications. It can be used in multipoint conferences.
H.323 terminal is compatible with H.324 terminals on PSTN, H.310 terminals on B-ISDN, H.320 terminals on ISDN, H.321 terminals on B-ISDN and H.322 terminals on QoS LAN.

## Slide 5: H.323 Gateway
H.323 gateway connects two dissimilar networks. For example, a gateway can connect and provide communication between an H.323 terminal and PSTN networks.
A connectivity of dissimilar networks is achieved by translating protocols for call setup and release, converting media formats between different networks and transferring information between the networks.
A gateway is not required for communication between two H.323 terminals.

## Slide 6: H.323 Gatekeeper
H.323 gatekeeper is an optional component in the H.323 network that provides a number of services to terminals, gateways and MCU devices.
Address resolution is the most important service as it enables two endpoints to contact each other without either endpoint having to know the IP address of the other endpoint.
H.323 endpoints use RSA protocol to communicate with a gatekeeper. Likewise, a gatekeeper uses RSA to communicate with other gatekeepers.

## Slide 7: H.323 Multipoint Control Unit
H.323 MCU is responsible for managing multipoint conferences. It consists of two logical entities, i.e., Multipoint Controller (Call signaling, conference control) and Multipoint Processor (switching/mixing of media streams).
An MCU manages conference resources, negotiates between terminals in order to determine the audio and video CODEC, and may handle the media stream. Some MPs can do real-time transcoding of the received audio/video streams.
The gatekeepers, gateways and MCU can be implemented in a single physical device.

## Slide 8: H.323 Multipoint Control Unit
Text: T.140
Video: H.26x
Audio: G.711, G.729
G.723,G.726
IP
UDP
TCP/UDP
H.225 Call Signaling
H.245
H.225 RAS
RTCP
RTP
CODEC
TCP
UDP
Media Control
Terminal Control & Management
Multimedia Applications, User Interface

## Slide 9: H.225
H.225 Call Signaling is used to establish a connection between two H.323 endpoints. This is achieved by exchanging H.225 protocol messages between two H.323 endpoints or between an endpoint and the gatekeeper.
H.225 RSA (Registration, Admission, and Status) is the protocol between endpoints and gatekeepers. RSA messages perform registration, admission control, bandwidth changes, status, and disengage procedures between endpoints and gatekeeper. The signaling channel is opened prior to the establishment of any other channels.

## Slide 10: H.225 Call Signaling
Message | Description
Setup | This is sent by H.323 caller to indicate its desire to set up a connection to the callee.
Call Proceeding | This is sent by the callee to indicate that it has received all the information it needs to route the call to its destination.
Alerting | This message might be sent by the callee to indicate that the callee is being alerted of the incoming call, i.e., the phone is ringing.
Connect | This is sent by the callee to the caller to indicate that the call has been accepted.
Release Complete | This is sent by either callee or caller to indicate the call’s release.
Notify | This is used to notify a device of a change that has occurred in the call.
Status Inquiry | This can be used to request call status.
Status | This is used to respond to an unknown call signaling or a Status Inquiry message.
… | …

## Slide 11: H.225 RSA
Gatekeeper Discovery Gatekeeper Request (GRQ) Gatekeeper Confirm (GCF) Gatekeeper Reject (GRJ) | Registration Registration Request (RRQ) Registration Confirm (RCF) Registration Reject (RRJ)
Admission Control Admission Request (ARQ) Admission Confirm (ACF) Admission Reject (ARJ) | Unregistration Unregistration Request (URQ) Unregistration Confirm (UCF) Unregistration Reject (URJ)
Disengage Disengage Request (DRQ) Disengage Confirm (DCF) Disengage Reject (DRJ) | Endpoint Location Location Request (LRQ) Location Confirm (LCF) Location Reject (LRJ)

## Slide 12: H.245
H.245 control signaling is used to exchange end-to-end control messages, governing H.323 operation.
Master/Slave Determination Master-Slave Determination Master-Slave Determination Ack. | Logical Channel Signaling Open Logical Channel Open Logical Channel Ack.
Close Logical Channel Signaling Close Logical Channel Close Logical Channel Ack. | Bidirectional Logical Channel Signaling Open Logical Channel Open Logical Channel Ack.
Ending a session End Session | Capabilities Exchange Terminal Capability Set Terminal Capability Set Ack. Terminal Capability Set Reject

## Slide 13: H.323 Call Flow
1
2
3
4
5,6
7
8
9
10
11
12
13
(RTP/RTCP)
H. 225
H. 245
H. 245
H. 225
Setup
Call Proceeding
Alerting
Connect
Capability Exchange
Master-Slave Determination
Open Logical Channel
Open Logical Channel Ack.
Open Logical Channel
Open Logical Channel Ack.
End Session
End Session
Release Complete
TER. A
TER. B

## Slide 14: H.323 Call Flow (Cont.)
1
2
3
4
5
6
7
8
9
10
11
12
…
GK
(RTP/RTCP)
H.245
ARQ
ACF
Setup
ARQ
ACF
Alerting
Connect
Release Complete
DRQ
DCF
DRQ
DCF
TER. A
TER. B

## Slide 15: H.323 Call Flow (Cont.)
1
4
5
6
7
8
9
10
11
12
13
14
…
GK
ARQ
LRQ
LCF
ACF
Setup
ARQ
ACF
Alerting
Connect
Release Complete
DRQ
DCF
DRQ
DCF
GK
2
3
TER. A
TER. B

## Slide 16: H.323 Call Flow (Cont.)
1
4
Gateway
H.225 Setup
Q.931 Setup
Q.931 Call Proceeding
H.225 Call Proceeding
H.225 Alerting
Q.931 Connect
H.225 Connect
Q.931 Connect Ack.
Q.931 Disconnect
H.245 End Session
H.245 End Session
Q.931 Release
Q.931 Release Complete
H.225 Release Complete
2
3
PSTN
Ring
5
Off-Hook
6
7
8
(RTP/RTCP)
TDM Stream
On-Hook
H.245
9
10
11
14
12
13
TER. A
TER. B

## Slide 17: H.323 Ad-Hoc Conference
1
2
3
Media Exchange
Setup
Connect
Capability Exchange
Master-Slave Determination
Logical Channel Establishment
Setup
Connect
Capability Exchange
Master-Slave Determination
Logical Channel Establishment
With MCU
4
5
6
7
8
9
10
Multipoint Conference
TER. A
TER. B

## Slide 18: Session Initiation Protocol
Dr. Quang Duc Tran

## Slide 19: SIP Definition
Session Initiation Protocol (IETF RFC 3261) is an application layer control (signaling) protocol for creating, modifying and terminating multimedia sessions across packet networks.
The main signaling functions of SIP are as follows:
  Location of an endpoint
  Contacting an endpoint to establish a session
  Exchange of media information to establish a session
  Modification of existing media sessions
  Teardown of existing media sessions

## Slide 20: SIP Definition (Cont.)
SIP is highly extensible. It can be extended to accommodate features and services such as call control services, interoperability with existing telephony systems, and more.
A SIP network consists of four types of logical SIP entities, i.e., User Agent (UA), Gateway, Back-to-back UA, Proxy Server, Redirect Server and Registrar. Each entity has specific functions and participates in SIP communication as a client (initiating requests), as a server (responding to requests), or as both.

## Slide 21: SIP User Agent
A UA takes input from a user and acts as an agent on his behalf to set up and tear down media sessions with other UAs. The user can be a human or another protocol (e.g., gateway). UAs typically register with a proxy server in their domain.
RFC 2543 defines UA as an application that contains both UA Client (UAC) and UA Server (UAS). UAC is a client application that initiates SIP requests. UAS is a server application that contacts the user when a SIP request is receiving and returns a response on behalf of the user.

## Slide 22: SIP Server
A SIP Proxy Server receives a request from a UA or another proxy and acts on behalf of the UA in forwarding or responding to the request. It does not issue requests and has no media capabilities. Stateful proxy server (e.g., forking proxy server) keeps track of requests and responses received in the past.
A SIP Redirect Server accepts a SIP request, maps the SIP address of the callee into zero (if there is no known address) or a new address and returns it to the UA. It does not pass the request to other servers.
A SIP Registrar Server accepts REGISTER requests for the purposes of updating a location database with the contact information of the user, specified in the request.

## Slide 23: SIP Back-to-back User Agent
A B2BUA is a type of UA that receivers a SIP request, then reformulates the request and sends it out as a new request.
B2BUAs act like a proxy but do not follow proxy routing rules. B2BUAs are call-stateful while proxy servers are transaction-stateful. Proxy server keeps state only during SIP transactions (i.e., at the beginning and end of a call) and do not keep any state during the whole call.
B2BUAs can be a part of many devices (e.g., PBX). Conference bridge and mixers also use B2BUA logic.

## Slide 24: SIP Gateway
A SIP gateway is an application that interfaces a SIP network to a network utilizing another signaling protocol. SIP gateway is a special type of UA, there the UA acts on behalf on another protocol.
A SIP gateway may be decomposed into (1) a media gateway (MG) that manages call control protocols, and (2) a media gateway controller (MGC) that manages the media connection.
A SIP gateway can support hundreds of users.

## Slide 25: SIP Requests
Message | Description
INVITE | Initiates a call, changes call parameters (re-INVITE)
ACK | Confirms a final response for INVITE
BYE | Terminates a call
CANCEL | Cancels searches and “ringing”
OPTIONS | Queries the capabilities of the other side
REGISTER | Registers with the Location Service
INFO | Send mid-session information that does not modify the session state
UPDATE | Modifies the state of a session without changing the state of the dialog

## Slide 26: SIP Responses
Class | Description
1xx | Informational (Indicates the status of the call prior to completion)
2xx | Success (The request has succeeded)
3xx | Redirection (The server has returned possible locations)
4xx | Client error (The request has failed due to an error by the client)
5xx | Server failure (The request has failed due to an error by the server)
6xx | Global failure (The request has failed, and should not be tried at this or other server)
Trying 301 Move Permanently 402 Payment Required
180 Ringing 302 Move Temporarily 403 Forbidden
OK 400 Bad request 404 Not found
Accepted 401 Unauthorized 503 Service Unavailable
300 Multiple Choices 402 Payment Required 604 Does Not Exist Anywhere

## Slide 27: SIP Call Flow
INVITE
180 - Ringing
200 - OK
ACK
BYE
200 - OK
(RTP/RTCP)
Registrar
Location
REGISTER
401 Unauthorized
REGISTER
200 - OK
Sip: name@hust.com
Credentials
UA A
UA B
UA A

## Slide 28: SIP Call Flow (Cont.)
Redirect Server
UA A
UA B
INVITE
302 - Moved
ACK
BYE
200 - OK
(RTP/RTCP)
INVITE
200 - OK
ACK
Proxy Server
UA A
UA B
INVITE
100 - Trying
(RTP/RTCP)
INVITE
180 - Ringing
180 - Ringing
180 - Ringing
200 - OK
200 - OK
BYE
200 - OK
200 - OK
BYE
ACK
ACK

## Slide 29: SIP Call Flow (Cont.)
Gateway
UA A
Proxy Server
INVITE
100 - Trying
180 - Ringing
INVITE
180 - Ringing
200 - OK
200 - OK
ACK
ACK
UA B
PSTN
Q.931 Setup
Q.931 Call Pro.
Ring
Off-Hook
Q.931 Connect
Q.931 Con. Ack.
(RTP/RTCP)
TDM Stream
On-Hook
Q. 931 Dis.
Q.931 Release
Q.931 Re. Com.
BYE
200 - OK
200 - OK
BYE

## Slide 30: SIP Call Flow (Cont.)
MCU
UA A
UA C
INVITE
180 - Ringing
200 - OK
ACK
(RTP/RTCP)
UA B
(RTP/RTCP)
NOTIFY (UA B in Conference)
200 - OK
SUBSCRIBE
200 - OK
NOTIFY
200 - OK
INVITE