## Slide 1: RTP, RTCP & RTSP
Dr. Quang Duc Tran

## Slide 2: Multimedia Traffic
Real-time
Multimedia Traffic
Real-time
Traffic
Multimedia
Traffic
The production, transmission, and use of data take place at the same time
The production, transmission, and use of data take place at different times
Streaming Live A/V
(Broadcast TV/radio via Internet)
Can not pause, rewind. The time between request and display is from 1 to 10 seconds.
Real-Time Interactive A/V
(IP Phone, Video conferencing)
Can not pause, rewind. The time between request and display is small
(video<150 ms and audio<400 ms)
Streaming Stored A/V
(Like VoD)
May pause, rewind… The time between request and display is from 1 to 10 seconds.

## Slide 3: Real-Time Multimedia Traffic
The use of timestamps may overcome the jitter problem. Each packet has a time of the packet with respect to the first packet.
The playback is delayed 7s after receiving the first packet.
Playback buffer is needed to separate playback time from the arrival time.
Server
Client
Server
Client
10s
0s
20s
30s
11s
1s
21s
31s
10s
0s
20s
30s
15s
1s
27s
37s
Jitter: The gap between received packets
Note that delay is not constant
7s

## Slide 4: Playback Point
D = ED + β EV
Where
  D: Playback Point
  ED: Estimated average packet delay
  EV: Estimated average packet delay variation
  β: Safety Factor (β=4)
EDi = α EDi-1 + (1 - α) (ri - ti)
EVi = α EVi-1 + (1 - α) (ri - ti - EDi)
Where
  α: Weighting Factor (α=0.998)
  ri : Time the packet i is received
  ti : Timestamp of the packet i

## Slide 5: Why Real-Time Data Can Not Be TCP?
TCP forces the sink application to wait for retransmission(s) in the case of packet loss, causing large delays.
TCP cannot support multicast, which is a basic requirement of video conferencing applications.
TCP congestion control mechanisms decreases the congestion window when packet losses are detected. Audio and video on the other hand have bitrates that cannot be suddenly decreased.

## Slide 6: Why Real-Time Data Can Not Be TCP?
TCP headers are larger than a UDP header.
TCP does not contain the timestamp and encoding parameters, needed by the receiver.
TCP does not allow packet loss. In A/V, a loss of 1-20% is tolerable. The loss can be compensated by FEC.

## Slide 7: Multimedia Protocol Stack
AAL3/4
IP Version 4, IP Version 6
UDP
Media encaps
(H.264, MPEG-4)
RTP
ATM/Fiber Optics
Ethernet/WIFI
TCP
SIP
RTSP
RSVP
RTCP
AAL5
MPLS
DCCP
DASH
HTTP
Synchronization Service

## Slide 8: Real-Time Transport Protocol
RTP is a network protocol for delivering audio and video over IP network. RTP is used in conjunction with the Real-Time Control Protocol (RTCP). While RTP carries the media streams, RTCP is used to monitor transmission statistics and QoS and aids synchronization of multiple streams.
RTP does not ensure real-time delivery, but it provide means for
  Jitter elimination/reduction by using playback buffer.
  Synchronization of several audio and video streams.
  Multiplexing of audio and video streams.
  Translation of audio and video streams.

## Slide 9: Real-Time Transport Protocol
Ver. | P | X | Contr. Count | M | Payload Type | Sequence Number
Timestamp |  |  |  |  |  | 
Synchronization Source Identifier |  |  |  |  |  | 
Contributor Identifier |  |  |  |  |  | 
… |  |  |  |  |  | 
Contributor Identifier |  |  |  |  |  | 
Version Number (2)
Padding Bit (1 – Packet contains padding)
Extension bit (1- Fixed header is followed by an extension header)
Marker bit (1 – The frame boundary is marked)
Incremented for each RTP packets (it is used to indicate packet loss and packet sequence)
ID of the source that is generating the RTP packets
It is used by a mixer to identify the contributing sources
UDP Header | RTP Header | RTP Payload | Padding | Pad Count

## Slide 10: Timestamp and Sequence No.
Audio
  RTP packet caries 20 ms of audio samples. Timestamp clock rate for audio is 8000 Hz. Hence, timestamp increments by 160.
  No. of bits per RTP payload for uncompressed audio is 160x8=1280. That for compressed audio is typically 8 times less.
Video
  RTP packet caries one video frame. RTP packet rate is 25 or 30 Hz. Timestamp clock rate for video is 90,000 Hz. Hence, timestamp increments by 3600 or 3000.
  No. of bits per RTP payload for uncompressed video conferencing is 352x240x12 = 10000

## Slide 11: Timestamp Clock Rate
Name | Type | Clock rate (Hz) | Frame size (ms) | Packet size (ms) | Description | References
PCMU | Audio | 8000 | any | 20 | ITU-T G.711 PCM | RFC 3551
GSM | Audio | 8000 | 20 | 20 | European GSM 13 kbps | RFC 3551
G722 | Audio | 8000 | any | 20 | ITU-T G.722 64 kbps | RFC 3551
L16 | Audio | 44100 | any | 20 | Linear PCM 16 bit stereo | RFC 3551
G729 | Audio | 8000 | 10 | 20 | G.729, G.729a 8 kbps | RFC 3551
raw | Video | 90000 |  |  | Uncompressed video | RFC 4175
H.263 | Video | 90000 |  |  | H.263, 1st-3rd version | RFC 3551 RFC 4629 RFC 2190
H.264 | Video | 90000 |  |  | H.264 AVC, H.264 SVC | RFC 3984 RFC 6190
JPEG | Video | 90000 |  |  | JPEG2000 video | RFC 5371

## Slide 12: Real-Time Control Protocol
RTCP provides out-of-band statistics (e.g., packet loss, packet delay variation, round-trip delay time) and control information for an RTP session.
The functionalities of RTCP include:
  Gathering statistics on quality aspects of the media distribution and transmitting this data to the session media source and other session participant.
  Provisioning session control functions. RTCP is a convenient means to reach all session participants. RTP is only transmitted by a media source.

## Slide 13: Real-Time Control Protocol (Cont.)
UDP Header
RTCP Packet
RTCP Packet
RTCP Packet
RTCP Header
RTCP Data
Version | P | RR Count | Packet Type | Message Length
Number of Reception Report Blocks, contained in the packet
Padding bit
200: SR (Sender Report)
201: RR (Receiver Report)
202: SDES (Source Description)
203: BYE
204: APP (Application Specific Message)
207: XR (RTCP Extension)

## Slide 14: Real-Time Control Protocol (Cont.)
Sender Report (SR)
  It is sent periodically by the active senders to report transmission and reception statistics. The report include an absolute timestamp, allowing the receiver to synchronize RTP messages. (Note: video and audio streams use independent relative timestamps).
Source Description (SDES)
  It is used to send CNAME item to session participant that provides additional information such as the name, e-mail address, telephone number of the owner of the source.

## Slide 15: Real-Time Control Protocol (Cont.)
Receiver Report (RR)
  It informs the sender and other receivers about the QoS.
Goodbye (BYE)
  A source sends a BYE message to shut down a stream. It also allow an endpoint to announce that it is leaving the conference.
Application Specific Message (APP)
  The application-specific message provides a mechanism to design application-specific extensions to the RTCP protocol.

## Slide 16: Real-Time Control Protocol (Cont.)
The volume of RTCP traffic may exceed the RTP traffic during a conference session involving large number of participants. This is because RTCP packets are sent regardless whether participant is talking or not.
RTCP traffic is dynamically changed depending of the number of participants. Typically, it is designed to be no more than 5% of the RTP traffic (1.25% allocated to sender, and 3.75% allocated to receivers). As number of receivers increases, frequency of response per receiver decreases.

## Slide 17: Forward Error Correction
D1
D2
D3
DN-1
….
P1
P1 = XOR(D1, D2,D3,…,DN-1)
D3 = XOR(D1, D2,…,DN-1,P1)
D1
D2
Dk
….
P1
P2
PN-k
….
P1 is called Parity Packet
The Parity Packets can help to recover the loss of any N-k out of N packets (Reed Solomon Erasure Code).
FEC increases the required bandwidth and latency.
FEC

## Slide 18: Interleaving
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
1
Original RTP packets, each contains 20 ms of voice samples
5
9
13
2
6
10
14
3
7
11
15
4
8
12
16
1
2
4
5
6
8
9
10
12
13
14
16
Lost packet causes 5 ms gaps in the audio stream, which can not be noticed. Interleaving does not increase the bandwidth, but increases delays.

## Slide 19: Receiver-Based Repair
1
2
3
4
1
2
3
4
Receiver-Based Repair does not increase the bandwidth requirement nor delays. It works with small packets and is based on the assumption that there is a small difference between two neighboring packets (voice packets).
Packet is recovered by interpolation, which can be computationally expensive and small delay.

## Slide 20: Secure Real-Time Transport Protocol
SRTP provide confidentiality, message authentication, and replay protection to the RTP and RTCP traffic.
With appropriate key management, SRTP is secure for unicast and multicast RTP applications.
Secure RTCP (SRTCP) provides the same security services to RTCP as SRTP does to RTP

## Slide 21: Secure Real-Time Transport Protocol
MKI (Master Key Identifier) is defined and used by key management.
The MKI identifies the master key from which the session key(s) are derived that authenticate and/or encrypt the packets.
Each SRTP stream requires the sender and receiver to maintain cryptographic state information, which is called the cryptographic context.

## Slide 22: Secure Real-Time Transport Protocol
A packet is replayed when it is stored by an adversary, and then re-injected into the network.
When message authentication is provided, SRTP protects against such attacks by using a Replay List. Each SRTP receiver maintains a Replay List, which conceptually contains the indices of all the packets which have been received and authenticated.

## Slide 23: Real-Time Streaming Protocol
RTSP is a network control protocol (port number is 554), designed for controlling streaming media servers. It is used to establish and control media session between end-points. Most RTSP servers use the RTP and RTCP for media stream delivery.
RTSP defines control sequences useful in controlling multimedia playback and uses TCP to maintain end-to-end connection. Unlike HTTP, RTSP has state. Request can be made by both the streaming server and client.

## Slide 24: Real-Time Streaming Protocol (Cont.)
Control Request | Description
SETUP | Asks the server to allocate resources for a stream and start an RTSP session.
PLAY | Starts data transmission on the allocated stream.
RECORD | Initiates recording a range of media data.
PAUSE | Temporarily halts a stream without freeing the allocated resources.
TEARDOWN | Frees resources associated with the stream.
ANNOUNCE | Changes description and media object.
REDIRECT | Redirects request to inform the client to connect to another server location.
SET_PARAMETER | Sets the value of a parameter for a presentation or stream.
DESCRIBE | Gets description of media object.

## Slide 25: Real-Time Streaming Protocol (Cont.)
Web Browser
Web Server
Media
Player
Media
Server
Presentation Description File
HTTP Get
SETUP
PLAY
PAUSE
TEARDOWN
Media Stream
The Web Server or HTTP Server serves Web pages. The Streaming Server or Media Server, serves the audio/video files.
The two servers can run on the same end system or on two distinct end systems.
Media Player and Streaming Server can interact using RTSP.

## Slide 26: Real-Time Streaming Protocol
Benefits: Low-latency and requires no buffering.
Drawbacks: Not optimized for QoE and scalability.
Latency: 2 seconds.
Variant Formats: The entire stack of RTP, RTCP and RTSP is often referred to as RTSP.

## Slide 27: Real-Time Messaging Protocol
RTMP was initially a protocol developed by Macromedia for streaming audio, video and data over the Internet between Flash player and a server.
The plain protocol uses TCP port number 1935.
RTMPS is RTMP over a TLS/SSL connection. RTMPE is RTMP encrypted using Adobe’s own security mechanism. RTMPT is encapsulated within HTTP requests to traverse firewall. RTMFP is RTMP over UDP instead of TCP.

## Slide 28: Real-Time Messaging Protocol
Benefits: Low-latency and requires no buffering.
Drawbacks: Not optimized for QoE and scalability.
Latency: 5 seconds.
Variant Formats: RTMPT (tunneled through HTTP), RTMPE (encrypted), RTMPTE (tunneled and encrypted), RTMPS (encrypted over SSL), RTMFP (travels over UDP instead of TCP).

## Slide 29: HTTP Live Streaming
HTTP Live Streaming (known as HLS) is an HTTP-based adaptive bitrate streaming communication protocol, developed by Apple Inc.
Based on standard HTTP transaction, HLS can traverse any firewall or proxy server that lets through standard HTTP traffic.
The standard also include a standard encryption mechanism and secure-key distribution using HTTPS.

## Slide 30: HTTP Live Streaming
Benefits: Adaptive bitrate and widely supported.
Drawbacks: QoE is prioritized over low latency.
Latency: 6-30 seconds.
Variant Formats: Low Latency HLS (3 seconds or less), PHLS (Protected HLS).

## Slide 31: MPEG-DASH
MPEG-DASH (Dynamic Adaptive Streaming over HTTP) is an industry-standard alternative to HLS.
Benefits: Vendor independent, international standard.
Drawbacks: Not supported by iOS or Apple TV.
Latency: 6-30 seconds.
Variant Formats: MPEG-DASH CENC (Common Encryption).

## Slide 32: WebRTC
WebRTC is a combination of standards, protocols and JavaScript APIs that enables real-time communications. With Chrome, Edge, Firefox and Safari supporting WebRTC, more than 85% of all installed browsers globally have become a client for real-time communications.
Benefits: Sub-500-millisencond delivery (Super fast and browser-based).
Drawbacks: Designed for video conferencing and not scale.