## Slide 1: MULTIMEDIA NETWORKING SYSTEM
Dr. Quang Duc Tran

## Slide 2: User Requirements
Fast preparation and presentation of the different multimedia types of interest, taking into account the capabilities of available terminals and services.
Dynamic control of multimedia applications with respect to connection interactions and quality on demand, combined with user-friendly interfaces.
Intelligent support of users, taking into consideration their individual capabilities.

## Slide 3: Network Requirements
High speed and changing bandwidth
  Multimedia applications, particularly those using video and images demand large bandwidth. However, bandwidth for the foreseeable future will be limited. The limitation arise from the cost of installing optical fiber transmission, terminal equipment complexity and speed, etc.
Quality of Services
  The availability of multimedia sources places demands on the service that a network must provide. The most importance of these is the bit error rate, the packet or cell loss, delay and delay variation.

## Slide 4: Network Requirements (Cont.)
Synchronization of different information types
  Multimedia synchronization refers to temporal relationships between the media objects. A common example of temporal relationship is movie or television, where both audio and video objects are involved.
Reliable security features and firewalls
  Security features include digital watermarking, data hiding, multimedia content protection, biometrics, multimedia human-computer interface.
  Firewall refers to a system, which controls the incoming and outgoing network traffic based on an applied rule set.

## Slide 5: MULTIMEDIA NETWORKS
Dr. Quang Duc Tran

## Slide 6: Multimedia Networks
Wide-Area Network (WAN)
  Typically, a WAN consists of a number of interconnected switching nodes. It covers a broad area using leased telecommunication lines. Conventionally, WANs have been implemented using one of two technologies, i.e., circuit switching and packet switching.
Local Area Network (LAN)
  A LAN interconnects computers within a limited area. Hence, the scope of LAN is typically a single building or a cluster of buildings. The internal data rates of LANs are much greater than those of WANs.

## Slide 7: LAN Technology
Features | FDDI | Ethernet | Token Ring
Transmission rate | 125 MBAUD | 20 MBAUD | 8 & 32 MBAUD
Data rate | 100 Mbps | 10 Mbps | 4 & 16 Mbps
Signal encoding | 4B/5B 80% Efficient | Manchester 50% Efficient | Diff. Manchester 50% Efficient
Maximum coverage | 100 km (UTP, Fiber) | 2.5 km (Coax., UTP, Fiber) | Configuration dependent
Maximum nodes | 500 | 1024 | 250
Maximum distance between nodes | 2 km (MMF) 40 km (SMF) | 2.5 km | 300 m recommended 100 m
FDDI: Fiber Distributed Data Interface

## Slide 8: FDDI Properties
FDDI uses a ring topology of multimode or single mode optical fiber transmission links operating at 100 Mbps to span up to 100 km and permits up to 500 stations.
To accommodate a mixture of stream, FDDI is designed to handle two types of traffic:
  Synchronous frames that typically have tighter delay requirements (e.g., voice and video).
  Asynchronous frames that have greater delay tolerances (e.g., data traffic).
FDDI uses TTRT (Target Token Rotation Time) to ensure that token rotation time is less than some value.

## Slide 9: FDDI Layers
Logical Link Control (LLC)
Media Access Control (MAC)
Physical (PHY)
Physical medium dependent (PMD)
Station Management
(SMT)
Data Link Layer
Physical Layer

## Slide 10: FDDI Layers
Physical Layer provides the media independent functions associated with the OSI physical layer. Its functionalities also include decoding and encoding (PMD to a symbol stream and data and control symbols to PMD).
MAC layer provides fair (i.e., no node has higher priority than others in accessing the medium) and deterministic access (i.e., under error-free conditions, the time a node has to wait to access the medium can be predicted)
SMT is a sophisticated, built in network monitoring and management capabilities. It is not an OSI-RM specification.

## Slide 11: FDDI Advantages
High Bandwidth (100 Mbps)
Large distance between FDDI nodes because of very low attenuation (≤0.3 dB/km) in fibers.
Improved Signal-to-Noise ratio because of no interference from external radio frequencies and electromagnetic noise
Bit error rate (10-11) is substantially better than that in Copper (10-5) and microwave system (10-7).
Very difficult to tap signal from a fiber cable.

## Slide 12: FDDI Limitations
High cost of optical components required for transmission/reception of signals (especially for single mode fiber network)
More complex to implement than existing low speed LAN technologies such as Ethernet and Fast Ethernet.

## Slide 13: WAN Technology
Public Switched Telephone Network (PSTN)
Integrated Service Digital Network (ISDN)
Broadband ISDN
Wireless Network (note: wireless LAN)
Broadcast Channel: Terrestrial, Cable, Satellite.

## Slide 14: PSTN
Now known as Plain Old Telephone Service (POTs)
The term switched means a subscriber can make a call to any other telephone on the ‘total’ network.
The copper wire between the home and central office has a limited bandwidth (56 Kbps). This is still too low for carrying video with pleasing quality.
Higher data rates, up to 6 Mbps in the downlink direction are possible with ADSL (Asymmetric Digital Subscriber Loop) modems. ADSL is one of the main transport media for streaming MPEG-1, MPEG-2 movies through VOD services.

## Slide 15: ISDN
ISDN is the first network using digital transmission. The data rate can be multiples of basic channels (B channels) of 64 Kbps each, with multiplying factor ranging from 1 to 24.
The basic subscription of ISDN comes with a 2B+D channel, where D channel is 16 Kbps and is used for return signaling. At 128 Kbps, very low quality video can be achieved.
ISDN connection is very reliable. H.320 (i.e., the first recommendation series for audio-video conferencing) was developed for ISDN.

## Slide 16: Broadband ISDN
B-ISDN services offer H.0 channels (384 Kbps), H.11 channels (1.536 Mbps) and H.12 channels (1.920 Mbps). This requires higher bandwidth coaxial cable or optical fiber.
B-ISDN uses Asynchronous Transfer Mode (ATM) packet switching with fixed size packets (known as cells). The very short cell size (53 Bytes with 48 Bytes payload) makes B-ISDN suitable for real-time applications with low delay requirements.
Cell loss can occur due to traffic congestion, although the loss (10-6-10-4) is quite low for video services.

## Slide 17: Why the Cell Size is 53 Bytes?
The cell size is determined as a trade-off between packetizing delay and cell overhead. Generally, cell overhead (waste) is smaller at larger payload sizes.
However, small cell size is preferred because of cell loss. For example, a 53 Bytes cell contain 48 voice samples, which is only 48 x 125 µs = 6 ms of voice. The loss of a cell would be almost unnoticed. However, a loss of cell with 32 ms of voice would be very disruptive.
32 Byte is the maximal payload size, at which there is no noticeable packetizing delay, but the overhead would be 13.5%. 64 Bytes payload would produce a small echo in voice communication, but the overhead would be 7.1%.

## Slide 18: ATM Service Categories
Constant Bit Rate (CBR)
  CBR supports real-time applications that require tightly constrained delay and delay variation (e.g., video conferencing, telephone call, video/audio distribution).
Variable Bit Rate (VBR)
  Real-time VBR supports real-time applications, but may allow more efficient use of a network.
  Non Real-time VBR supports real-time applications, which are more tolerant of network delays (e.g., airline reservations, banking transactions, process monitoring)

## Slide 19: ATM Service Categories (Cont.)
Available Bit Rate (ABR)
  ABR is a best effort service, which supports non real-time applications that allow congestion control because the sender can be informed to slow down the traffic in congestion periods (e.g., critical data transfer, text/data/image retrieval and distribution, remote terminal).
Unspecified Bit Rate (UBR)
  UBR is a best effort service without any performance requirement. UBR is equivalent to Internet.

## Slide 20: Wireless Network
Network | Data Rate | Mobility | Range | Channel Quality
Cellular Network | <20 Kbps | High | 2.5 km | Poor
Wireless Data Network | 64-384 Kbps | High | 2.5 km | Poor
Wireless LAN | 2-25 Mbps | Low (Indoor) | 50 m | Location dependent
Wireless IP Network | 1-600 Mbps downlink | Low (Indoor) | 3-30 miles | Good
Cellular Network: GPRS, EDGE (8.8-59.2 Kbps)
Wireless Data Network: 3G (BER <10-6)
Wireless IP Network (2.15-40 GHz): MMDS (1 Mbps), LMDS (600 Mbps)
Notes: MMDS: Multichannel Multipoint Distribution Service, which is used as replacement of cable TV service provider in rural areas. (2.15 GHz – 2.68 GHz, OFDM, 521 sub carriers, 12 kHz per sub carrier, 50-100 km, 1-10 Mbps). MMDS is ideal for small business enterprises. Due to larger wavelength MMDS is less susceptible to rain.
LMDS: Local Multipoint Distribution Service, which is used to provide TV and 2 way internet service (30 GHz-40 GHz, 2 to 8 km, up to 2 Mbps). LMDS offers higher data rates.

## Slide 21: Wireless Network (Cont.)
Difficulties for video transport over wireless networks lie in the low bandwidth, high error rate, and most importantly, the fluctuation of available bandwidth and error characteristics.
For real-world applications, quite sophisticated FEC (Forward Error Check) codes are used to reduce the bit error rates significantly.
Most wireless interactive multimedia communication systems employ H.223. H.223 conveys media data including compressed video in the form of packets of variable size. Typical packet sizes are around 100 bytes to ensure good delay characteristics.

## Slide 22: 3G Wireless System
3G provide higher data rates by using higher carrier frequencies, wider bandwidth and more sophisticated techniques for multiple access, error control, and signal detection.
BER for data transmission is below 10-6.
Generally, wireless channel is quite noisy with high bit error rates. But the use of rate adaptation, FEC and ARQ yield an almost error-free environment for data transmission. For video transmission, where ARQ has to be limited, one has to cope with quite high bit error rates and packet loss rates.

## Slide 23: Broadcast Channels
This is used for broadcasting of digital TV including HDTV using the MPEG-2 video coding and transport streams.
The compressed data are carried over packets of 188 bytes each. The MPEG-2 transport layer ensure an almost error free environment.
For SDTV, the available bandwidth is between 3-10 Mbps. For HDTV, 20 Mbps is typically allocated.

## Slide 24: Video Application Characteristics
Application and Standard Family | Multiplex Protocol | Video Coding Standard | Bit Rate | Error Characteristics
ISDN Video Phone (H.320) | H.221 | H.261 and H.263 | 64-384 Kbps | Error free
PSTN Video Phone (H.324) | H.223 | H.263 | 20 Kbps | Very low
Mobile Video Phone (H.324 wireless) | H.223 | H.263 | 10-300 Kbps | BER = 10-5-10-3 Occasional packet loss
Video Phone over Packet network (H.323) | H.225/RTP/ UDP/IP | H.261 H.262 H.263 | 10-1000 Kbps | BER = 0, 0-30% packet loss
Satellite TV | MPEG-2 System | MPEG-2 | 6-12 Mbps | Almost error free
Video conferencing over ATM (H.320, H.321) | H.222 | H.262 | 1-12 Mbps | Almost error free
H.262 is identical to MPEG-2 video, H.222 is identical to MPEG-2 system